## Slide 1: W26 Cobot Axis
UR30 7th Axis for Metal Paste Dispensing
ME 472 — Mechatronics, Winter 2026
Willem Bell (Software / EE) · Dawood _____ (Mechanical)
April 24, 2026
Notes: 60-second hook. "The UR30 is a 6-axis collaborative robot. We built it a 7th axis — a stepper-driven pump for metal paste dispensing — that takes commands directly from the robot controller in real time. Over the next 15 minutes we'll walk through how we got there, using Bolton's seven-step design process as the backbone."

## Slide 2: The Need
  UR30 collaborative robot — no native mechanism for an external coordinated motion axis
  Metal-paste additive manufacturing requires a pump synchronized to TCP velocity
  Commercial UR+ accessories: expensive, proprietary, not tuned for paste
  Digital I/O alternative: on/off only — no speed synchronization
  Goal: external stepper axis that takes commands from the UR30 controller in real time, dispenses metal paste, reports status
Notes: Motivation. Under-fill during acceleration, over-fill during deceleration — bead quality suffers without coordinated extrusion. No off-the-shelf solution for this in the lab.

## Slide 3: Problem Analysis — Bolton Step 2
  Only real-time interface out of UR30: RTDE on TCP port 30004, 500 Hz (register-based, no motion semantics)
  Latency tolerance: 20 ms worst-case — at 50 mm/s TCP, that's 1.0 mm bead position error (within 1–5 mm bead width)
  Power: 2 A continuous / 3.5 A burst @ 24 V from UR30 controller — hard limit
  Failure modes: RTDE loss, stepper stall, 24 V fault, Klipper crash, USB disconnect — all must drive safe-state within one RTDE cycle
Notes: RTDE exposes 48 INT + 48 DOUBLE + 64 BOOL registers per direction. All coordination logic — clamping, mode handling, watchdog — lives outside the UR30. Paste dispensing is forgiving compared to FDM; that forgiveness is what makes sub-ms latency unnecessary.

## Slide 4: Design Specification — Bolton Step 3
  25 functional requirements (FR-01 through FR-25) — extrusion control, status, safety, homing, connection management
  10 constraints (C-01 through C-10) — power, driver limits, platform choices
  Performance targets: P95 latency < 20 ms, e-stop < 1 RTDE cycle, watchdog 500 ms
  6 output + 5 input RTDE registers allocated (minimal; ample headroom)
  Parameters awaiting hardware: motor current/torque, pump displacement, paste viscosity — bounded ranges only
Notes: Full spec in docs/design_specification.md. TBD parameters are bounded with acceptable ranges so design space doesn't collapse while waiting for the motor/pump to arrive.

## Slide 5: Solution Space — Bolton Step 4
Three weighted-scoring trade studies:
Each scored against criteria weighted by update rate, latency, ecosystem, development time, cost
  Comm protocol: RTDE vs Modbus TCP vs Primary Interface vs URScript Socket vs XML-RPC vs Dashboard
  Firmware framework: Klipper vs Lingua Franca
  MCU platform: BTT SKR Pico vs raw RP2040 Pico vs Arduino + CNC Shield vs Teensy 4.1
Notes: Full matrices in trades/*.md. Weighted scoring is important here — we had strong intuition about the winners but wanted to force ourselves to document why alternatives were rejected.

## Slide 6: Trade Study Results
  RTDE: native UR30 support, 500 Hz, bidirectional
  Klipper: proven motion planning + 100 ms lookahead buffer
  SKR Pico: TMC2209 soldered, Klipper-native, on hand
Decision | Winner | Score | Runner-up | Score
Comm protocol | RTDE | 4.85 | Modbus TCP | 3.30
Firmware framework | Klipper | 4.70 | Lingua Franca | 1.95
MCU platform | SKR Pico V1.0 | 5.00 | Raw RP2040 Pico | 3.00
Notes: All three winners "click" together — RTDE and Klipper are both well-supported on the Raspberry Pi side, and the SKR Pico is Klipper's reference RP2040 board. The coherence is part of why the architecture works.

## Slide 7: Selected Architecture
```
UR30 ──RTDE/TCP 500 Hz──▶ Pi (bridge daemon + Klipper) ──USB 12 Mbps──▶ SKR Pico ──STEP/DIR──▶ TMC2209 ──▶ Stepper ──▶ Pump
```
  UR30: URScript on teach pendant writes 6 RTDE output registers
  Pi: Python bridge daemon (125 Hz) + Klipper host (100 ms lookahead) + Unix socket to klippy
  SKR Pico (RP2040): Klipper MCU firmware, 4x TMC2209 soldered, USB-C + 24 V in
  Feedback: 5 RTDE input registers (status, error code, actual rate, ready, fault)
  Pi400: optional HMI / SSH / Mainsail — not in the real-time loop
Notes: The dotted box around "Pi" hides complexity — inside it are two processes (bridge daemon, klippy) talking over a Unix socket. Pi400 was originally in the path as a slave serial bridge; we removed it after the Klipper trade made direct USB viable.

## Slide 8: Electrical Design
Budget: 1.0 A typical / 1.4 A peak at 24 V — fits in 2 A UR30 continuous limit with 1 A margin
  24 V from UR30 power block → 3 A fuse → SMBJ24CA TVS → 100 µF bulk cap
  Direct to SKR Pico VIN (logic + TMC2209 VMOT)
  Pololu D24V22F5 buck → 5.1 V @ 2.2 A → Pi GPIO header (behind 2 A PTC polyfuse)
  Signal: Ethernet (RTDE), USB-C (Klipper serial), 4-wire motor cable
  Pin assignments: gpio14 STEP, gpio13 DIR, gpio15 EN, UART addr 3 (gpio8/9)
Notes: Every protection component has a reason: fuse for catastrophic short, TVS for the UR30 power block switching transients, bulk cap for motor current pulses, polyfuse because the Pi GPIO path bypasses the onboard fuse.

## Slide 9: Software Architecture
  URScript on UR30: writes mode/rate/enable/e-stop/home to output registers at 500 Hz
  Bridge daemon (Python, 11 modules, 479 tests, 100 % coverage):
  `rtde_client` (reads) → `bridge_daemon` state machine → `klipper_client` (writes G-code)
  `watchdog` stops stepper if no RTDE data in 500 ms
  `extrusion_profile` — linear / polynomial / lookup-table rate shaping
  `klipper_status` polls TMC2209 diagnostics at 20 Hz
  Klipper on Pi: motion planning + 100 ms MCU lookahead buffer
  Klipper firmware on RP2040: 16x microstepping, StealthChop mode
Notes: Single-threaded, synchronous by design — predictable timing beats throughput. Stateless translator between two async systems. All 479 tests run in ~1.5s, no hardware needed.

## Slide 10: Latency Model
  20 ms × 50 mm/s = 1.0 mm bead position error — within tolerance
  Klipper's 100 ms lookahead adds latency but eliminates step-timing jitter
Segment | Typical (ms) | Worst (ms)
UR30 RTDE cycle | 0–2 | 4
Ethernet + switch | 0.1–0.5 | 1
Bridge (Python) | 0.5–2 | 5
Klipper host | 0.5–2 | 5
USB serial | 1–3 | 5
MCU step gen | <0.1 | 0.5
Total | ~5–8 | ~20
Notes: The Klipper lookahead is a latency/precision tradeoff we chose intentionally — at the MCU level, step timing is microsecond-precise even though the Linux host has 1-10 ms scheduling jitter.

## Slide 11: Stretch Goal: StallGuard Torque Feedback
  TMC2209 has a DIAG pin that asserts in microseconds when load crosses the StallGuard threshold
  Klipper polls over UART at ~4 Hz — 250 ms blind window for stall damage
  Our solution: dedicated firmware on RP2040's idle Core1
  Core1 monitors DIAG pin in hardware, debounces, stores event + timestamp in shared SRAM
  Core0 (Klipper) serves `stallguard_query` / `stallguard_clear` MCU commands
  Klippy extras module polls at 20 Hz → RTDE input register → URScript can halt robot on stall
  Safe spinlock #16, zero impact on Klipper step timing
  Validated by `docs/design/hitl_plan.md` TP-06
Notes: This also satisfies the "sensors" element of the ME472 course prompt. The DIAG signal path is hardware-speed detection that survives the 250ms poll gap.

## Slide 12: Testing and Validation
  Functional: `test_basic.script` — 9 sub-tests (init, enable, extrude, retract, home, e-stop, speed-sync, fault, status)
  Latency: oscilloscope from UR30 digital output to SKR Pico gpio14 step pulse
  Accuracy: commanded vs measured rate @ 5, 10, 25, 50 mm/s; gravimetric paste dispensed
  Fault injection: RTDE disconnect, Klipper shutdown, stall, power loss
  Stretch: StallGuard HITL (TP-06) — DIAG event reaches URScript in ≤ 100 ms
  CI/CD: Tier 1 lint+test+shellcheck on every commit; Tier 2 firmware cross-compile; weekly patch-freshness against upstream Klipper
Notes: All software testing is mock-based — 479 tests run in 1.5s with zero hardware. Hardware-dependent tests wait on the motor/pump delivery.

## Slide 13: Results vs Specification
Status: software and firmware complete; hardware integration pending motor/pump delivery
Target | Result
End-to-end latency < 20 ms P95 | 5–8 ms predicted; measurement deferred to Phase 4
E-stop response < 2 ms | Implemented; measurement deferred
Watchdog < 500 ms | Implemented, 100 % tested
Power draw < 2 A @ 24 V | 1.0 A typ / 1.4 A peak predicted
Speed accuracy < 5 % | Deferred to hardware
479 unit tests @ 100 % coverage | Achieved
Notes: Hedge honestly — we have a fully validated software stack, a detailed electrical design, and a stretch-goal firmware overlay that's written and unit-tested, but we don't yet have measured latency numbers on the real motor.

## Slide 14: Lessons Learned — Bolton Process in Practice
  Step 2 ↔ Step 4 iteration was real: the original "slave Pi as serial bridge" architecture died once the Klipper trade study made direct USB viable → saved 0.12 A, one point of failure
  Specification tightened after driver research: TMC2209 is thermally limited to 0.8 A without cooling, not 1.2 A — forced a cooling-fan line item
  Hardware-free development is viable: `FakeKlippy` mocks + `ur_rtde` stub → 479 tests run with zero hardware in 1.5 s
  CI/CD pays for itself: patch-freshness workflow catches Klipper upstream drift weekly before it breaks our overlay
Notes: The Bolton iteration is a feature, not a defect. We wrote about this explicitly in Section H of the report — the specification is better for having been revised.

## Slide 15: Future Work
  Full pump + paste characterization on delivered hardware
  Measured latency + accuracy numbers (Phase 4 completion)
  Multi-material support (swap paste cartridges mid-print)
  URCap for teach-pendant UI (Java SDK, not needed for MVP)
  Predictive G-code timeshifting using Klipper's 100 ms lookahead buffer
  Production StallGuard tuning with real paste loads
Notes: The capstone ends April 23, but the project has a life beyond — particularly the multi-material and URCap work that a future team could pick up.

## Slide 16: Thank You — Questions?
Repo: github.com/wrbell/W26-Cobot-Axis
Team: Willem Bell (Software/EE) · Dawood _____ (Mechanical)
Advisor: Prof. Pannier
Key references:
  W. Bolton, Mechatronics, 7th ed., Pearson, 2019
  SDU Robotics, ur_rtde library
  Klipper3D documentation
  BTT SKR Pico V1.0 user manual; Trinamic TMC2209 datasheet
Notes: Leave 2-3 minutes for Q&A. Likely question topics: latency measurement methodology, why Klipper over ROS/custom, metal paste specifics (defer to instructor-provided info), safety story under fault conditions.

## Slide 17: Backup: Bill of Materials
Full BOM with DigiKey/Newark part numbers: `docs/phase2/bom.md`
Category | Items | Cost
Electronics (Pi, buck, switch, cables) | 7 | $148.79
Protection + passives | 6 | $3.65
Wiring + connectors | 7 | $30.45
On hand (SKR Pico, Pi 400, PSU) | 3 | $0
Provided (motor, pump) | 2 | $0
3D-printed (enclosure, mount, clips) | 3 | $0
Total | 28 | ~$183

## Slide 18: Backup: Power Budget
Device | Idle | Typical | Peak | Notes
Pi (via buck, 90% eff) | 0.15 A | 0.35 A | 0.45 A | 1.5 A @ 5.1 V design
SKR Pico (logic) | 0.05 A | 0.08 A | 0.10 A | RP2040 + TMC2209 quiescent
Stepper motor | 0.10 A | 0.50 A | 1.00 A | TBD placeholder NEMA 17
Cooling fan (opt.) | 0.00 A | 0.04 A | 0.08 A | If TMC2209 cooling required
Total | 0.30 A | ~0.97 A | ~1.63 A | vs 2.0 A / 3.5 A UR30 budget

## Slide 19: Backup: RTDE Register Map
UR30 → Pi (output)
Pi → UR30 (input)
Reserved: StallGuard load, driver temperature, position target
  `output_int_register_0` — extrusion mode (0/1/2)
  `output_double_register_0` — commanded rate (mm/s)
  `output_double_register_1` — TCP speed (mm/s)
  `output_bit_register_64/65/66` — enable / e-stop / home
  `input_int_register_0` — status (0 idle / 1 running / 2 error / 3 homing)
  `input_int_register_1` — error code (0/1/2/3)
  `input_double_register_0` — actual rate (mm/s)
  `input_bit_register_64/65` — ready / fault